## Slide 1: CATIA V5R21 Persistent Naming
16-05-18
Soonjo Kwon
iCAD

## Slide 2: Document History
16-05-18_Soonjo Kwon_Draft
16-10-11_Soonjo Kwon_r1

## Slide 3: Table of Contents
CATIA Persistent Naming
Face Naming
Edge Naming
Key information
  Sketch element
Naming mapping
Conclusion

## Slide 4: CATIA Persistent Naming
CATIA uses topology-based persistent naming method
  Face naming is the basis
    Required Information for face naming
      Face type (initial, lateral, terminal)
      Feature name
      Sketch name, Sketch element number
    For edge or vertex, adjacent faces are used for naming
  ※ The following content is based on CATIA V5R21

## Slide 5: Face Naming (1)
("Selection_RSur:( Face:(Brp:(Pad.1;2);None:();Cf11:()); Pad.1_ResultOUT;Z0;G4074)")
Face naming
Additional
Face naming
Key information
Recently created feature name

## Slide 6: Face Naming (2)
("Selection_RSur:( Face:(Brp:(Pad.1;0:(Brp:(Sketch.1;4)));None:();Cf11:()); Pad.1_ResultOUT;Z0;G4074)")
Face naming
Additional
Face naming
Key information
Recently created feature name

## Slide 7: Edge Naming (1)
("REdge:( Edge:( Face:(Brp:(Pad.1;0:(Brp:(Sketch.1;3)));None:();Cf11:()); Face:(Brp:(Pad.1;2);None:();Cf11:()); None:(Limits1:();Limits2:());Cf11:()); WithTemporaryBody;WithoutBuildError;WithSelectingFeatureSupport; MFBRepVersion_CXR15)", pad1)
First adjacent face naming
Second adjacent face naming
Additional
Edge naming
Face naming
Key information
Recently created feature name
edge
naming

## Slide 8: Edge Naming (2)
("TgtEdge:(GeneratedEdges;MfIE_R20GA;TgtPropagationFillet; FirstOperands:(Pad.1);SecondOperands:();InitEdges:REdge:( Edge:( Face:(Brp:(Pad.1;0:(Brp:(Sketch.1;3)));None:();Cf11:()); Face:(Brp:(Pad.1;2);None:();Cf11:()); None:(Limits1:();Limits2:());Cf11:()); WithTemporaryBody;WithoutBuildError;WithSelectingFeatureSupport; MFBRepVersion_CXR15)))", pad1)
First adjacent face naming
Second adjacent face naming
Additional
Edge naming
Face naming
Key information
Recently created feature name
Feature name of the target body
edge
naming

## Slide 9: Key information
(Pad.1;0:(Brp:(Sketch.1;3)))
Feature name
Face type
0 : lateral face
1 : initial (start) face
2 : terminal (end) face
Sketch information (In case of lateral faces)
Sketch name
Sketch element number (=ReportName)
(* Initial or terminal face requires no sketch information)
(** Need two sketch information for the features that require two sketches such as rib, slot)
(Rib.1;0:(Brp:(Sketch.1;4);Brp:(Sketch.2;3)))

## Slide 10: Key information : Sketch element
ReportName is used to identify a sketch element
  Dim line2D1 As Line2D
  Set line2D1 = factory2D1.CreateLine(-20.000000, -20.000000, 20.000000, -20.000000)
  line2D1.ReportName = 3
  ……
  line2D2.ReportName = 4
  ……
  line2D3.ReportName = 5
  ……
  line2D4.ReportName = 6
Sketch.1
line2D1
line2D4
line2D3
line2D2
Create Pad.1
(Pad.1;1)
(Pad.1;0:(Brp:(Sketch.1;3)))
(Pad.1;0:(Brp:(Sketch.1;4)))
(Pad.1;0:(Brp:(Sketch.1;5)))
(Pad.1;0:(Brp:(Sketch.1;6)))
(Pad.1;2)
An example of
CATIA macro

## Slide 11: Naming mapping
Select an edge
Naming mapping is necessary for translating reference elements such as face, edge, vertex
TgtEdge:(GeneratedEdges;MfIE_R20GA;TgtPropagationFillet; FirstOperands:(Pad.1);SecondOperands:();InitEdges:(REdge:( Edge:( Face:(Brp:(Pad.1;0:(Brp:(Sketch.1;3)));None:();Cf11:()); Face:(Brp:(Pad.1;2);None:();Cf11:()); None:(Limits1:();Limits2:());Cf11:()); WithTemporaryBody;WithoutBuildError; WithSelectingFeatureSupport;MFBRepVersion_CXR15)))
Extrude1,Sketch1,Line3,0,0,0,ExtrudeFeature:0,0:0;0#
Extrude1,0,-2,0,0,0,ExtrudeFeature:0,0:0;0
Create a fillet
CATIA
TransCAD
mapping

## Slide 12: Conclusion
CATIA is using topology-based persistent naming
Face naming is the basis
  Key information: Feature name, Face type, Sketch information
Sketch information consists of sketch name & sketch element number
  ReportName is used to identify a sketch element (=sketch element number)
To understand the persistent naming method is the key for implementation
  Naming mapping between two CAD systems is mandatory for translation

## Slide 13: Conclusion
Please check all the face names of all the additive/subtractive features in CATIA
  Use macro recording function
The naming rule of TransCAD is almost similar with the naming rule of CATIA
  The naming method is thought to be version-independent, but please check if the naming method is the same when you upgrade CATIA