## Slide 1: CATIA V5R21 Persistent Naming
11 April 2018
Soonjo Kwon, Imgyu Kim
iCAD

## Slide 2: Document History
16-05-18_Soonjo Kwon_Draft
16-10-11_Soonjo Kwon_r1
4/11/2018 Imgyu Kim
  –Add Instruction of CATScript for assembly model.

## Slide 3: Table of Contents
CATIA Persistent Naming
Face Naming
Edge Naming
Key information
  Sketch element
Naming mapping
Naming for assembly
Conclusion

## Slide 4: CATIA Persistent Naming
CATIA uses topology-based persistent naming method
  Face naming is the basis
    Required Information for face naming
      Face type (initial, lateral, terminal)
      Feature name
      Sketch name, Sketch element number
    For edge or vertex, adjacent faces are used for naming
  ※ The following content is based on CATIA V5R21

## Slide 5: Face Naming (1)
("Selection_RSur:( Face:(Brp:(Pad.1;2);None:();Cf11:()); Pad.1_ResultOUT;Z0;G4074)")
Face naming
Additional
Face naming
Key information
Recently created feature name

## Slide 6: Face Naming (2)
("Selection_RSur:( Face:(Brp:(Pad.1;0:(Brp:(Sketch.1;4)));None:();Cf11:()); Pad.1_ResultOUT;Z0;G4074)")
Face naming
Additional
Face naming
Key information
Recently created feature name

## Slide 7: Edge Naming (1)
("REdge:( Edge:( Face:(Brp:(Pad.1;0:(Brp:(Sketch.1;3)));None:();Cf11:()); Face:(Brp:(Pad.1;2);None:();Cf11:()); None:(Limits1:();Limits2:());Cf11:()); WithTemporaryBody;WithoutBuildError;WithSelectingFeatureSupport; MFBRepVersion_CXR15)", pad1)
First adjacent face naming
Second adjacent face naming
Additional
Edge naming
Face naming
Key information
Recently created feature name
edge
naming

## Slide 8: Edge Naming (2)
("TgtEdge:(GeneratedEdges;MfIE_R20GA;TgtPropagationFillet; FirstOperands:(Pad.1);SecondOperands:();InitEdges:REdge:( Edge:( Face:(Brp:(Pad.1;0:(Brp:(Sketch.1;3)));None:();Cf11:()); Face:(Brp:(Pad.1;2);None:();Cf11:()); None:(Limits1:();Limits2:());Cf11:()); WithTemporaryBody;WithoutBuildError;WithSelectingFeatureSupport; MFBRepVersion_CXR15)))", pad1)
First adjacent face naming
Second adjacent face naming
Additional
Edge naming
Face naming
Key information
Recently created feature name
Feature name of the target body
edge
naming

## Slide 9: Key information
(Pad.1;0:(Brp:(Sketch.1;3)))
Feature name
Face type
0 : lateral face
1 : initial (start) face
2 : terminal (end) face
Sketch information (In case of lateral faces)
Sketch name
Sketch element number (=ReportName)
(* Initial or terminal face requires no sketch information)
(** Need two sketch information for the features that require two sketches such as rib, slot)
(Rib.1;0:(Brp:(Sketch.1;4);Brp:(Sketch.2;3)))

## Slide 10: Key information : Sketch element
ReportName is used to identify a sketch element
  Dim line2D1 As Line2D
  Set line2D1 = factory2D1.CreateLine(-20.000000, -20.000000, 20.000000, -20.000000)
  line2D1.ReportName = 3
  ……
  line2D2.ReportName = 4
  ……
  line2D3.ReportName = 5
  ……
  line2D4.ReportName = 6
Sketch.1
line2D1
line2D4
line2D3
line2D2
Create Pad.1
(Pad.1;1)
(Pad.1;0:(Brp:(Sketch.1;3)))
(Pad.1;0:(Brp:(Sketch.1;4)))
(Pad.1;0:(Brp:(Sketch.1;5)))
(Pad.1;0:(Brp:(Sketch.1;6)))
(Pad.1;2)
An example of
CATIA macro

## Slide 11: Naming mapping
Select an edge
Naming mapping is necessary for translating reference elements such as face, edge, vertex
TgtEdge:(GeneratedEdges;MfIE_R20GA;TgtPropagationFillet; FirstOperands:(Pad.1);SecondOperands:();InitEdges:(REdge:( Edge:( Face:(Brp:(Pad.1;0:(Brp:(Sketch.1;3)));None:();Cf11:()); Face:(Brp:(Pad.1;2);None:();Cf11:()); None:(Limits1:();Limits2:());Cf11:()); WithTemporaryBody;WithoutBuildError; WithSelectingFeatureSupport;MFBRepVersion_CXR15)))
Extrude1,Sketch1,Line3,0,0,0,ExtrudeFeature:0,0:0;0#
Extrude1,0,-2,0,0,0,ExtrudeFeature:0,0:0;0
Create a fillet
CATIA
TransCAD
mapping

## Slide 12: Conclusion
CATIA is using topology-based persistent naming
Face naming is the basis
  Key information: Feature name, Face type, Sketch information
Sketch information consists of sketch name & sketch element number
  ReportName is used to identify a sketch element (=sketch element number)
To understand the persistent naming method is the key for implementation
  Naming mapping between two CAD systems is mandatory for translation

## Slide 13: Conclusion
Please check all the face names of all the additive/subtractive features in CATIA
  Use macro recording function
The naming rule of TransCAD is almost similar with the naming rule of CATIA
  The naming method is thought to be version-independent, but please check if the naming method is the same when you upgrade CATIA

## Slide 14: CATScript file for Assembly model
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Design */
…
////////////////////////////////////////////////////////
/* Part #n Document 생성 */
////////////////////////////////////////////////////////
/* Part #n Design */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub
Same as a case of part translator

## Slide 15: CATScript file for Assembly model
////////////////////////////////////////////////////////
/* Product Document 생성 */
Dim documents1 As Documents
Set documents1 = CATIA.Documents
Dim productDocument1 As Document
Set productDocument1 = documents1.Add("Product")
Dim product1 As Product
Set product1 = productDocument1.Product
Dim products1 As Products
Set products1 = product1.Products
////////////////////////////////////////////////////////
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Design */
…
////////////////////////////////////////////////////////
/* Part #n Document 생성 */
////////////////////////////////////////////////////////
/* Part #n Design */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub

## Slide 16: CATScript file for Assembly model
////////////////////////////////////////////////////////
/* Part Document 생성 */
Dim product2 As Product
Set product2 = products1.AddNewComponent("Part", "")
Dim partDocument1 As Document
Set partDocument1 = documents1.Item("Part1.CATPart")
Dim part1 As Part
Set part1 = partDocument1.Part
Dim bodies1 As Bodies
Set bodies1 = part1.Bodies
Dim body1 As Body
Set body1 = bodies1.Item("PartBody")
////////////////////////////////////////////////////////
/* Part Design */
Dim sketches1 As Sketches
Set sketches1 = body1.Sketches
... 생략
part1.Update
////////////////////////////////////////////////////////
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Design */
…
////////////////////////////////////////////////////////
/* Part #n Document 생성 */
////////////////////////////////////////////////////////
/* Part #n Design */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub
주의!
모든 Entities의 numbering이 중복되면 안됨.

## Slide 17: CATScript file for Assembly model
Dim constraints1 As Collection
Set constraints1 = product1.Connections("CATIAConstraints")
Dim reference1 As Reference
Set reference1 = product1.CreateReferenceFromName(“…”)
Dim reference2 As Reference
Set reference2 = product1.CreateReferenceFromName(“…”)
Dim constraint1 As Constraint
Set constraint1 = constraints1.AddBiEltCst(catCstTypeSurfContact, reference1, reference2)
Set constraints1 = product1.Connections("CATIAConstraints")
Dim reference3 As Reference
Set reference3 = product1.CreateReferenceFromName(“…”)
Dim reference4 As Reference
Set reference4 = product1.CreateReferenceFromName(“…”)
Dim constraint2 As Constraint
Set constraint2 = constraints1.AddBiEltCst(catCstTypeOn, reference3, reference4)
product1.Update
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Design */
…
////////////////////////////////////////////////////////
/* Part #n Document 생성 */
////////////////////////////////////////////////////////
/* Part #n Design */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub

## Slide 18: CATScript file for Assembly model
Dim constraints1 As Collection
Set constraints1 = product1.Connections("CATIAConstraints")
Dim reference1 As Reference
Set reference1 = product1.CreateReferenceFromName(“…”)
Dim reference2 As Reference
Set reference2 = product1.CreateReferenceFromName(“…”)
Dim constraint1 As Constraint
Set constraint1 = constraints1.AddBiEltCst(catCstTypeSurfContact, reference1, reference2)
Set constraints1 = product1.Connections("CATIAConstraints")
Dim reference3 As Reference
Set reference3 = product1.CreateReferenceFromName(“…”)
Dim reference4 As Reference
Set reference4 = product1.CreateReferenceFromName(“…”)
Dim constraint2 As Constraint
Set constraint2 = constraints1.AddBiEltCst(catCstTypeOn, reference3, reference4)
product1.Update
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Design */
…
////////////////////////////////////////////////////////
/* Part #n Document 생성 */
////////////////////////////////////////////////////////
/* Part #n Design */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub

## Slide 19: CATIA Macro… for Assembly
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 CATPart 불러오기 */
////////////////////////////////////////////////////////
/* Part #2 CATPart 불러오기 */
…
////////////////////////////////////////////////////////
/* Part #N CATPart 불러오기 */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub

## Slide 20: CATIA Macro… for Assembly
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 CATPart 불러오기 */
////////////////////////////////////////////////////////
/* Part #2 CATPart 불러오기 */
…
////////////////////////////////////////////////////////
/* Part #N CATPart 불러오기 */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub
///////////////////////////////////////////////////////////////////////////////////////////////////
/* Part #1 CATPart 불러오기 */
Dim arrayOfVariantOfBSTR1(0)
arrayOfVariantOfBSTR1(0) = "C:\Users\Imgyu Kim… *.CATPart"
products1.AddComponentsFromFiles arrayOfVariantOfBSTR1, "All"
///////////////////////////////////////////////////////////////////////////////////////////////////

## Slide 21: CATScript for Assembly model
Dim constraints1 As Collection
Set constraints1 = product1.Connections("CATIAConstraints")
Dim reference1 As Reference
Set reference1 = product1.CreateReferenceFromName(“…”)
Dim reference2 As Reference
Set reference2 = product1.CreateReferenceFromName(“…”)
Dim constraint1 As Constraint
Set constraint1 = constraints1.AddBiEltCst(catCstTypeSurfContact, reference1, reference2)
Set constraints1 = product1.Connections("CATIAConstraints")
Dim reference3 As Reference
Set reference3 = product1.CreateReferenceFromName(“…”)
Dim reference4 As Reference
Set reference4 = product1.CreateReferenceFromName(“…”)
Dim constraint2 As Constraint
Set constraint2 = constraints1.AddBiEltCst(catCstTypeOn, reference3, reference4)
product1.Update
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Design */
…
////////////////////////////////////////////////////////
/* Part #n Document 생성 */
////////////////////////////////////////////////////////
/* Part #n Design */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub

## Slide 22: CATScript for Assembly model
Dim constraints1 As Collection
Set constraints1 = product1.Connections("CATIAConstraints")
Dim reference1 As Reference
Set reference1 = product1.CreateReferenceFromName(“…”)
Dim reference2 As Reference
Set reference2 = product1.CreateReferenceFromName(“…”)
Dim constraint1 As Constraint
Set constraint1 = constraints1.AddBiEltCst(catCstTypeSurfContact, reference1, reference2)
Set constraints1 = product1.Connections("CATIAConstraints")
Dim reference3 As Reference
Set reference3 = product1.CreateReferenceFromName(“…”)
Dim reference4 As Reference
Set reference4 = product1.CreateReferenceFromName(“…”)
Dim constraint2 As Constraint
Set constraint2 = constraints1.AddBiEltCst(catCstTypeOn, reference3, reference4)
product1.Update
Language="VBSCRIPT"
Sub CATMain()
////////////////////////////////////////////////////////
/* Product Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Document 생성 */
////////////////////////////////////////////////////////
/* Part #1 Design */
…
////////////////////////////////////////////////////////
/* Part #n Document 생성 */
////////////////////////////////////////////////////////
/* Part #n Design */
////////////////////////////////////////////////////////
/* Assembly Design */
Constraint #1
Constraint #2
…
Constraint #n
////////////////////////////////////////////////////////
End Sub

## Slide 23: Translation of references for constraints
“Product1/Part2.1/!Selection_RSur:(Face:(Brp:(Pad.1;1);None:();Cf11:());Pocket.1_ResultOUT;Z0;G4162)"
“Product1/Part1.1/!Selection_RSur:(Face:(Brp:(Pad.1;2);None:();Cf11:());Pad.2_ResultOUT;Z0;G4162)"
"Product1/Part2.1/!Axis:(Selection_RSur:(Face:(Brp:(Pocket.1;0:(Brp:(Sketch.2;1)));None:();Cf11:());Pocket.1_ResultOUT;Z0;G4162))"
"Product1/Part1.1/!Axis:(Selection_RSur:(Face:(Brp:(Pad.2;0:(Brp:(Sketch.2;1)));None:();Cf11:());Pad.2_ResultOUT;Z0;G4162))"
SubAssembly1,RotationPart,Extrude1,0,-1,0,0,0,ExtrudeFeature:0,0:0;0
SubAssembly1,Body,Extrude1,0,-2,0,0,0,ExtrudeFeature:0,0:0;0
SubAssembly1,RotationPart,Cut1,Sketch2,Circle1,0,0,0,ExtrudeFeature:0,0:0;0
SubAssembly1,Body,Extrude2,Sketch2,Circle1,0,0,0,ExtrudeFeature:0,0:0;0
Incidence constraint
Coaxial
CATIA
TransCAD
CATIA
TransCAD